Assignment – 4

1. (20 marks) Build a 18-bit carry-select adder. Decide the number of groups and the size of
each group. Estimate the time delay of your design.

Ans.) 18-bit carry-select adder => n = 18

        Let the 18-bit carry select adder be divided into L groups, each group of length k1, k2,...kL,
        then, the following inequality holds:

        => 1 + (L (L-1)) / 2 ≥ 18 => L(L - 1) ≥ 34

        Since, L is an integer, the minimum value of L that satisfies the above relation is L = 7.
        Hence, the number of groups in the carry-select adder are 7.

        The group size of each group would then be k1 = 1, k2 = 1, k3 = 2, k4 = 3, k5 = 4, k6 = 5,
        k7 = 2

        For a group l of length kl it takes (l - 1) times 2Δ_G for its carry-in cj signal to be available.
        And the latency of kl-bit RCA is 2kl ΔG

0
        Hence, time delay of this design would be = 1ΔG + (7 - 1)2ΔG = 13 ΔG

A
FA

1ΔG
2ΔG
2ΔG

  Figure 1: Critical path for “Carry select” adder

HA
FA
FA
FA

0

FA
FA

 1
0

1

FA

2ΔG
FA
FA => Full Adder
HA => Half Adder

1

FA
FA
FA
FA

FA
FA

2ΔG

FA
FA

FA
FA
1
  0

FA
FA

  0

FA
FA
2ΔG

FA
FA
FA
FA
FA
FA

FA
FA

FA
FA
FA
FA

2ΔG

0
 1

  1

2. (20 marks) Build a 18-bit carry-skip adder. Decide the number of groups and the size of a
group. Estimate the time delay of your design.

Ans.) Let the following three time delays be defined:

        tr denote carry ripple time through one bit
        ts(k) denote the time to skip on group
        tb denote the time delay of an OR gate

        For a n-bit carry-skip adder, of n/k groups where k is the size of the group,

        Tcarry = (k – 1) tr + tb + ( n/k - 2 ) ( ts + tb ) + (k – 1) tr
        = ( 4k + 2n / k - 7) ΔG

        where tr = 2ΔG and tb = ts = ΔG

        Optimal size of k => kopt = sqrt{n over 2}

        Hence, for n = 18, kopt = 3 => Number of groups = n /kopt = 18 / 3 = 6

  Figure 2 : Showing the critical path for “Carry Skip Adder”

        => Size of the group = kopt = 3

        => Optimal time delay of the design, Topt = ( 4 kopt + 2n / kopt - 7) Δg
        = ( 4*3 + (2 * 18) / 3 - 7) Δg = 17Δg

3. (20 marks) Build a carry-save adder that performs X = A + B + C + D + E, where each
of operands A, B, C, D, and E has 4 bits. Draw a full diagram for the carry-save adder and
estimate the complexities using both (3, 2) and (2, 2) counters as building blocks. Explicitly
show a critical path.

Ans.) Since, A, B, C, D and E are 4 bit operands => A, B, C, D, E ∈ [0, 24 - 1] = [0-15]
        Hence, the sum of four such numbers will have no more than ( 5 x [0-15]) ⊂ [0, 27 – 1] i.e. 7 bits

      => Organize the architecture diagram in at most 7 columns.

    26 25 24 23 22 21 20

 A0 B0 C0
 A1 B1 C1
A2 B2 C2

 ( 3, 2)
 ( 3, 2)
 ( 3, 2)
 ( 3, 2)
 ( 3, 2)
 ( 3, 2)

A3 B3 C3

D2
 ( 3, 2)

 ( 3, 2)

 ( 3, 2)

 ( 3, 2)

 ( 3, 2)

 ( 3, 2)

 ( 3, 2)

“0”

 D1

D3

 E3

 E2

E1
E0
“0”

 D0

“0”
    FA

    FA

    FA

    FA

    FA

“0”

“0”

s0

s1
s2
s3
s4
s5
s6

 Figure 3: “Carry Save Adder” using (3,2) as building blocks

 The architecture complexities using only (3,2) or FA as building blocks are:

* Circuit complexity: C = 18(3,2)'s = 18 FA
* Critical path delay: T = 8 * (2ΔG) = 16 ΔG

A3 B3 C3
 A1 B1 C1

 A0 B0 C0
A2 B2 C2

 ( 3, 2)
 ( 3, 2)
 ( 3, 2)

 ( 3, 2)

D2
 D1
D3
 D0

 ( 2, 2)
 ( 3, 2)
 ( 3, 2)
 ( 3, 2)

 E3
 E2

E1
E0

 ( 2, 2)
 ( 3, 2)
 ( 3, 2)
 ( 3, 2)
 ( 2, 2)

s6
s5
s4
s3
s1
s2
 Figure 4: “Carry Save Adder” using (2,2) as building blocks
s0

    HA

    FA

    FA

    FA
    HA

 The architecture complexities using both (3,2) or FA and (2,2) or HA as building blocks are:

* Circuit complexity: C = 13(3,2)'s + 5(2,2)'s = 13 FAs + 5HAs
* Critical path delay: T = 6 (2ΔG) + 2(1ΔG ) = 14 ΔG

4. (20 marks) Consider multiplication of a 5-bit multiplicand A and a 4-bit multiplier X. Design a high-speed multiplier realizing this multiplication operation. Assume that (3, 2) and (2, 2) counters are used for carry save addition and carry-propagate addition. Show the steps in dot diagram or draw a block diagram for your design. How many (3, 2) and (2, 2) counters are required? Assume that ∆ (3,2) = 2∆ G and ∆ (2,2) = ∆ G . What is time delay of your multiplier?

Ans.) Let A = (a4a3a2a1a0) and X = (x3x2x1x0) then the product bits P = (p8p7p6p5p4p3p2p1p0) can be
        obtained as follows:

        a4 a3 a2 a1 a0
        x3 x2 x1 x0
        ---------------------------------------------------------------------
        a4x0 a3x0 a2x0 a1x0 a0x0
        a4x1 a3x1 a2x1 a1x1 a0x1
        a4x2 a3x2 a2x2 a1x2 a0x2
        a4x3 a3x3 a2x3 a1x3 a0x3
        ----------------------------------------------------------------------------------------------------------------------------
       p8 p7 p6 p5 p4 p3 p2 p1 p0

* The 20 partial product bits can be generated using 20 two-input AND gates and hence
   requires one gate delay

        * * * * *
        * * * * *
        * * * * *
        * * * * *
Figure 5: Dot diagram depicting the
        usage of (3,2)'s and (2,2)'s for
        adding the partial product terms

        ||

        * *
        * * * *
        * * * * * *
        * * * * * * * *

        || Applying 4 (3,2)'s (1-level CSA)

        * * *
        * * * * *
        * * * * * * * *

        || Applying 3 (3,2)'s and 1 (2,2) (1-level CSA)

        * * * * *
        * * * * * * * *
        || (CPA: 4 (3,2)'s and 3 (2,2)'s)

        * * * * * * * * *

* Let the partial product bit be denoted with a *. Then, the CSA tree of 20 partial product bits forms an isoceles trapezoid with 4 rows and base consisting of 8 asterisk's. Since, the height of the trapezoid is 4, it requires 2 levels of CSA before the final CPA.

* Number of (3,2) counter's required = 11
* Number of (2,2) counter's required = 4

a0x2
a1x2
a2x2

a1x1

a2x3

a2x0
a3x0
a2x1

a3x1

a3x2

a4x0

a4x1

 ( 3, 2)
 ( 3, 2)
 ( 3, 2)
 ( 3, 2)

 ( 2, 2)

 ( 2, 2)
 ( 2, 2)
 ( 3, 2)

 ( 3, 2)

 ( 3, 2)

Figure 6 : Block diagram depicting the usage of (3,2)'s and (2,2)'s for adding the partial product terms
a0x0
p0

p1

a0x1
a1x0

 ( 2, 2)

p2

a4x3

 ( 3, 2)
a3x3

a4x2

 ( 3, 2)

a1x3
  a0x3

 ( 3, 2)
p3
p4
p5
p6
p7
p8
 ( 3, 2)

* Time delay of the multiplier = Time to form the partial + Time for CSA to give actual product
        product terms (1 gate bits ( Critical path highlighted in red
        delay for the 2 input in Figure 6)
        AND gates)

        = 1 ΔG + (2 + 2 + 1 + 2 + 2 + 2 + 2) ΔG
        = 14ΔG

5. (20 marks) Consider multiplication of a 5-bit multiplicand A and a 4-bit multiplier X. Design
an array multiplier realizing this multiplication operation. Assume that FA and HA are used as
building cells. Draw a block diagram for your design. How many FAs and HAs are required?
Assume that ∆ FA = 2∆ G and ∆ HA = ∆ G . What is time delay of your design?

Ans.)

Let A = (a4a3a2a1a0) and X = (x3x2x1x0) then the product bits P = (p8p7p6p5p4p3p2p1p0) can be
        obtained as follows:

        a4 a3 a2 a1 a0
        * x3 x2 x1 x0
        ---------------------------------------------------------------------
        a4x0 a3x0 a2x0 a1x0 a0x0
        a4x1 a3x1 a2x1 a1x1 a0x1
        a4x2 a3x2 a2x2 a1x2 a0x2
       + a4x3 a3x3 a2x3 a1x3 a0x3
        ----------------------------------------------------------------------------------------------------------------------------
       p8 p7 p6 p5 p4 p3 p2 p1 p0

 Assuming that the partial product bits ai xj , i = 0,...,4 and j = 0,...,3, have been generated, an array multiplier realizing the multiplication operation can be designed using FA's and HA's as follows:

a1x0
a2x0
a3x0
a4x0
a0x0

HA => Half Adder

a4x3
 a3x3
a4x2
a2x3
a3x2
a4x1

FA
FA
FA
HA

a1x3
a2x2
a3x1
a1x2
a2x1
a0x2
a1x1
a0x1

HA
FA
FA
FA
FA
FA
FA
FA
HA
HA
FA
HA

FA => Full Adder
a0x3
 Figure 7 : Block diagram for multiplication of 5-bit multiplicand A and a 4-bit multiplier X
p8
p7
p6
p5
p4
p3
p2
p1
p0

* Number of Full Adder's required = 11
* Number of Half Adder's required = 5

* Time delay for the design = Time to form the partial + Time to get actual product
        product terms (1 gate bits ( Critical path highlighted in red
        delay for the 2 input in Figure 7)
        AND gates)

        = 1 ΔG + (1 + 2 + 2 + 1 + 2 + 2 + 2)ΔG
        = 13ΔG

6. (no marks) Let a residue number system (RNS) be given by (m2 , m1 , m0 ) = (15, 14, 13).
(a) Solve dynamic range for the RNS.
(b) Find the RNS representations for A = 1910 and B = 2210 . Perform C = A × B in the
RNS.
(c) How many bits are required to represent a number with respect to this RNS?

Ans.)

a) Dynamic range for the RNS(15,14,13), M = 15 * 14 * 13 = 15 * 182 = 2730
     => Range = [0, 2729]

b) RNS representation for A = 1910 is (19 % 15, 19 % 14, 19 % 13) = (4, 5, 6)
      RNS representation for B = 2210 is (22 % 15, 22 % 14, 22 % 13) = (7, 8, 9)
       C = A x B => C = (4*7, 5*8, 6*9)
        = (28, 40, 54)
        = (13, 12, 2) RNS (15,14,13)

c) Bits required to represent a number w.r.t this RNS = 4 + 4 + 4 = 12